## Slide 1: Water vapour and clouds
Important for:
  accurate precipitation forecasts.
  estimating surface energy budgets.
  assessing climate feedback effects.
Ground-based Raman lidar or Differential Absorption Lidar, space-borne lidar (but unable to measure water vapour under warm clouds.
Column water vapour values retrieved from Global Positioning Systems (GPS).
Satellites have enabled the development of two-dimensional cloud distributions using space-borne visible and infrared radiometers.
Vertical profiles of cloud and in-cloud droplet distributions not currently well measured (new space-based radar/lidar to address this).

## Slide 2: Precipitation
Primary input for hydrological cycle.
Crucial to understanding and predicting the Earth’s climate, weather, streamflow, soil moisture, and water availability.
Methods for measuring precipitation include:
  gauges
  surface- and satellite-based precipitation radars
  observations of passive microwave radiance from Low Earth Orbit (LEO) satellites
  infrared radiance observations of clouds from both LEO and Geostationary Earth Orbit satellites that enable retrievals of precipitation in the atmosphere.

## Slide 3: Evaporation and Evapotranspiration (ET)
Represent the moisture fluxes from the underlying ocean or land surface to the atmosphere.
Land-based ET reflects the rate of plant growth and drying of the surface.
Can be derived from:
  sea surface temperature estimates (ocean evaporation)
  land-based in-situ ET measurements (by Bowen ratio, eddy covariance, scintillometer)
  remote sensing methods as well as lysimetric and soil water balance methods.
Estimating ET and closing the water balance for the continental and global scales remains challenging.

## Slide 4: Soil moisture
Important for climate and water resources management.
Regulates the partitioning of incoming radiative energy into sensible and latent heat fluxes
Also partitions precipitation between infiltration, runoff, and evaporation
Can be derived from:
  In-situ networks
  remote sensing SMAP, SMOS

## Slide 5: River discharge
Measurements are essential for
  water management
  the design and operation of engineering works (dams, reservoirs, river regulation)
  various water-related services (navigation, flood protection, water supply for irrigation, municipal or industrial water use, ecosystem management).
Mainly in situ (some remote techniques emerging).

## Slide 6: Groundwater
Important source of water in many areas, is removed by natural processes (discharge) and groundwater pumping.
Replaced, in whole or in part, by recharge, which is at a maximum during wet periods.)
Groundwater measurements are collected in many countries but few countries share these data with the International Groundwater Assessment Centre (IGRAC), the designated global groundwater data centre.
Groundwater cannot be directly measured from satellite or other remote sensing systems, the measurement of gravity variations by the Gravity Recovery and Climate Experiment (GRACE) twin satellites can be related to groundwater variations when combined with a land surface model.

## Slide 7: Surface water storage
Source of drinking water, recreation, agricultural uses, hydro-electric power.
Home to aquatic ecosytems.
In situ and remote sensing measurements.
Standing water bodies are particularly poorly monitored due to their complex spatial configurations, combined with their innumerable occurrences and high temporal variability.
Reservoirs, with their known geometries, could be a more accurate means to monitor water bodies and fluxes; however, data exchange for reservoir operations is practically non-existent.

## Slide 8: Cryospheric variables
Needed to support climate studies and water resource management at mid and high latitudes.
Most convincing evidence of climate change comes from the reductions that have been reported in permafrost, seasonally frozen ground, river and lake ice, ice sheets and glaciers, and snow cover.
In situ networks exist, but are sparse (SNOTEL).
Satellite data on snow cover extent and snow water equivalent (SWE), primarily from Landsat, MODIS, GEOS, AVHRR, and AMSR satellites, provide geospatially consistent data for many key regions.
SWE, which is derived primarily from passive microwave measurements, is complicated by surface roughness, snow temperature, and other factors.

## Slide 9: Water quality
Suitability of water for various uses or processes where the standards for water quality are defined for each particular use.
Most significant cause of water quality degradation and subsequent decline of aquatic systems are human activities such as the discharge of untreated waste and industrial activities.
In-situ measurements are the basis for ensuring that local water complies with water quality standards.
Satellite remote sensing is emerging as a potential alternative for assessing some types of water quality.
  surface temperature, chlorophyll and cyanobacterial pigments, coloured dissolved organic material, Secchi disk transparency, turbidity and aquatic vegetation, and variables such as primary productivity and sediment fluxes

## Slide 10: Suspended sediments
River sediment transport strongly influences the quality and biodiversity of surface waters, riparian environments, and the functioning of coastal zones (nutrients, heavy metals, discharges).
Sediment data, which describe the wide range of sediment processes occurring in the environment, need to be collected, archived, and analyzed so that the linkages between river and lake processes and water quality can be fully understood.