## Slide 1
ODYSSEA project:
Data collection on water column
Sergio Martinez
Javier Martinez
November 2018

## Slide 2: About us
Applied research in Europe and South America
Spain
6 locations
Applied research
Chile
2 locations
Health & Biomedicine
Circular Economy
Energy + Engineering
Advanced Technological Solutions
Applied Chemistry & Materials
240 professionals
>220 R&D Contracts
>90% customer loyalty
22 million € revenue
odysseaplatform.eu |@odysseaplatform

## Slide 3: Business Units
Energy + Engineering
Circular Economy
Applied Chemistry & Materials
INDUSTRIAL
& SOCIETAL
INNOVATION
Health &
Biomedicine
Advanced
Technological
Solutions
Energy conversion & storage
Electronics & communication
Robotics
Product development
Nanomaterials
Polymers & Coatings
Lubs & Greases
Detergency & cosmetics
Waste valorization
Bioeconomy
Pollutants Control
Sustainability
Water Reuse
Analytical Chemistry
Inverse Engineering
Preclinical studies
Antibodies
Drug discovery
Diagnosis
odysseaplatform.eu |@odysseaplatform

## Slide 4: What we are working on
Studies of nanohealthy.
Concentration of some othe pollutants
Impact of nanoparticles on human health
Studies to determine particles on prawn & schrimp
Systems for water filtering on a WWTP
Characterization, separation and recovery
Use and evaluation of diferent techniques and equipment
FTIR
GPC-RI (Gel Permeation Chromotography – Refractive Index
MALDI – ToF / ToF
Mass spectrometry technique that used soft ionization
Allow the analysis of biomolecules: DNA, proteins, peptides
Methods to identify and quantify textile MP released during laundering of synthetic textiles
Influence of detergents
Influence of whashing conditions
Influence os textile topology
Using a Linitest apparatus (URAI S.p.A., Assago, Italy) for lab simulation of real washing machines operating in both domestic and industrial conditions
Design and development of automated systems
odysseaplatform.eu |@odysseaplatform

## Slide 5: Automated systems
What they should offer:
In-situ measurements
Real time mapping
Information availability
Decrease analysis time
Integration within existing platforms
  Ferry box / research vessels or boats
  Gliders
  Landers
  Surface platforms
But…
Diversity: Microplastics are not homogeneus, with a lot of inferents (aging, eutrophications, contaminants....)
Spatial range: If we plan to monitor wide areas, use of buffering and concentration tools are required. Otherwise maybe the sample is not significative.
Speed and size: It determines the resolution of system, in terms of computation speed and range of particles that can be identified.
odysseaplatform.eu |@odysseaplatform

## Slide 6: To consider previously
This is the most important part. How to perform a representative or a least an effective sample acquisition
How to diferentiate microplastics from other sources. (sand, algae, fishes…)
Provide all the numbers in order to give an idea about general concern of microplastics.
1. Sampling
2. Detection
3. Quantification
4. Study / conclusions
To determine how many of the detected particles are microplastics, and to enumerate them. If feasible provide a number in terms of concentration.
Reproducibility
y repeatability
In other to provide the same conclsuions in the same experiments (validation purposes).
Assays should be not destructive, in other to allow counter-analysis.
odysseaplatform.eu |@odysseaplatform

## Slide 7: Previous experience
COMMON SENSE was an Oceans of Tomorrow 2013 Project, devoted to provide innovative sensors, in order to meet MSFD
LEITAT developed a first prototype of an automated microplastics sensor for in-situ measurements.

## Slide 8: Previous experience

## Slide 9: Previous experience COMMON SENSE
odysseaplatform.eu |@odysseaplatform

## Slide 10: ODYSSEA project
odysseaplatform.eu |@odysseaplatform
ODYSSEA is a user-centred project aiming to make Mediterranean marine data easily accessible and operational to multiple end-users
ODYSSEA is a system bridging the gap between operational oceanography capacities and the need for information on marine conditions from the community of end-users.
ODYSSEA’s ambition is to develop an interoperable, fully-integrated and
cost-effective multiplatform network of observing and forecasting systems across the Mediterranean basin, addressing both the open sea and the coastal zone.

## Slide 11: ODYSSEA project
odysseaplatform.eu |@odysseaplatform

## Slide 12: Odyssea sensors: Where
odysseaplatform.eu |@odysseaplatform

## Slide 13: Sampling collection & Validation
odysseaplatform.eu |@odysseaplatform

## Slide 14: Sensor
Multiband system
Chart: 
odysseaplatform.eu |@odysseaplatform

## Slide 15
Sergio Martínez
Javier Martínez
smartineznavas@leitat.org
jmartinez@leitat.org
odysseaplatform.eu |@odysseaplatform
ODYSSEA